## Slide 1
Stakeholder consultation meeting on the review of the Seveso II Directive Brussels, 10 November 2009 Item 5: Views of Stakeholders (1) Industry obligations (2) The public (3) Application, Scope
DG ENV A4 Civil Protection – prevention and preparedness http://ec.europa.eu/environment/seveso/index.htm
Notes: 1

## Slide 2: Philosophy of Seveso II Directive
Safe
Management
Safe
Technology
Demonstrate safety
in the Safety Report
Emergency
Planning
Land-Use
Planning
Information to the Public
I N S P E C T I O N S
Accident Reporting and Lessons Learnt

## Slide 3: Scope & main obligations
Excluded Sector? (Article 4)
Seveso does not apply
What is the quantity of dangerous substances? (Annex I)
Lower than lower tier
Notification
Major Accident Prevention Policy (MAPP)
Domino Effects
Land-use planning
Inspection
Quantity above the lower threshold
Additionally:
Safety report (including MAPP and Safety Management System)
Emergency plans (internal and external)
Information to the public
Quantity above the
higher threshold
Yes
No
nuclear,
transport, military

## Slide 4: MAPP/SMS
Would it be appropriate to require Safety Management Systems (SMS) for all Seveso plants (Requirements proportionate to hazards - simplified SMS for LT)?
Should there be a clearer distinction between MAPP
and SMS obligations and between procedures and documentation?
Helpful to refer to other management systems like ISO, OSHAs, etc?
Possible use of SPI and safety culture indicators?
Notes: 4

## Slide 5: Safety Report
“Static” Report up-to-date? SMS and Internal Emergency Plan integrated or separated?
More harmonised tools for comparing reports and for risk assessment?
Are external accident causes (natural disasters, security issues, others) adequately addressed?
Notes: 5

## Slide 6: Information to the public
Is balance between public access and confidentiality right? (Directive on public access to environmental information/Aarhus Convention and security)?
How is dissemination of information monitored to ensure that information on requisite behaviour gets to all people liable to be affected? Improvements, internet era?
Are deadlines for review/updating/repetition of information still appropriate?
"eReporting" through databases at Member State level to cover implementation reports plus information to the public under Article 13.1/Annex V?
Notes: 6

## Slide 7: Emergency planning, Domino effects
Should co-operation with different authorities be improved? How could this be done in the Directive?
Ensure and improve consultation of the public and of subcontractors when plans are updated and tested?
Review Annex IV, need to develop guidance, exemption criteria, etc.?
Domino effects/Industrial Parks with Non-Seveso sites: Need for exchange of information, information on safety measures (art 13.1), hazard/risks in SR (Annex II)?
Notes: 7

## Slide 8: Land-Use Planning (LUP)
  How could co-operation between Seveso and planning authorities be improved?
  How to ensure that LT sites provide sufficient information (proportionate to the risk)?
  Calculating safety distances, would sharing of experience on methodologies be useful?
  Would possible closer integration with procedures under the EIA and SEA Directives be helpful?
  Strengthen risk communication?
Notes: 8

## Slide 9: Definitions, exclusions, readability
Definitions: Are there inconsistencies with other Directives causing problems?
Any exclusions that require clarifications?
General readability: Which provisions are unclear?

## Slide 10: Seveso Scope, Annex I - GHS
Separate amendment to Annex I of the Seveso II Directive
  Change reference to CLP Regulation1272/2008/EC
Technical Working Group: 1:1 Translation
    ~ 35 Members, ¾ Member States, ¼ Industry, stakeholders
    5/6 TWG meetings, draft interim report available
    Final meeting on 26/27 November
    Final Report in Winter
Notes: 10

## Slide 11: TWG Seveso and GHS - Draft “GHSified” Annex I Part 2
Section ‘H’ - HEALTH HAZARDS
H1 ACUTE TOXIC 1
H2 ACUTE TOXIC 2
H3 STOT SPECIFIC TARGET ORGAN TOXICITY – SINGLE EXPOSURE
Section ‘P’ - PHYSICAL HAZARDS
P1 OXIDIZING GASES
P2 OXIDIZING LIQUIDS AND SOLIDS
P3/P4 EXPLOSIVES
P5 FLAMMABLE GASES
P6/P7 FLAMMABLE AEROSOLS
P8/P9/P10 FLAMMABLE LIQUIDS
P11/P12 SELF-REACTIVE SUBSTANCES AND MIXTURES and ORGANIC PEROXIDES
P12 SELF-REACTIVE SUBSTANCES AND MIXTURES and ORGANIC PEROXIDES
P13 PYROPHORIC LIQUIDS
Section ‘E’ - ENVIRONMENTAL HAZARDS
E1/E2 Hazardous to the Aquatic Environment
Section ‘O’ – OTHER HAZARDS
O1/O2/O3 ANY CLASSIFICATION in combination with hazard statement:
EUH014,…,EUH029

## Slide 12: Comparison toxic properties
T+
T
Xn
EU
1
2
3
4
Oral
mg/kg
1
2
3
4
inhal.
vapour
mg/l
inhal.
aerosol
mg/l
1
2
3
4
2
3
4
inhal. gas
mg/l
ppm
1
3
2
4
Dermal
mg/kg
0
25
200
0
5
25
50
200
300
0
0,1
0
0
0
0,5
0,5
2
2.5
2
200
50
400
1000
0,5
0,05
0,25
1
500
2000
2500
100
0
10
1
2 +3+4
comparing line to old legislation
1+2 +3+4 for T+
1
Gyenes
A1
A2
A5
A3
A7
A6
A4

## Slide 13: Impact Assessment 1
Necessary where old categories in Seveso not fully match the new GHS categories; Procedure:
Develop options considering the hazard potential of substances
Estimate the likely impact of these options
  substances concerned (difficult for substances currently not in the scope; minimum classification – correct classification?)
  are these substances relevant in industry
  are they used in higher quantities
  number of establishments possibly covered (in/out)

## Slide 14: Impact Assessment 2
Commission: contract for an Impact Assessment study into possible options
Cooperation with the TWG
Analysis of the technical work and of possible options
Impact Assessment of options

## Slide 15: Effects GHS on Seveso
CLP Regulation itself:
Is there an impact on Seveso due to new categories, new definitions, new testing, better grid; change from preparations to mixtures (example: sodium hypochlorite)?
Translation by the TWG
Impact by not 1:1 translatable Categories?
Impact of different options assessed by the Impact Assessment Study?

## Slide 16: Other possible amendments to Annex I
Consider adding CO2 (CCS) as a named substance?
Review derogation clause/Safeguard clause?